## Slide 1
Ground to Rocket Launch
Rocket Ascent Trajectory
Orbit Insertion & Decay
3D Model of Balloon, Launch Structure
Weather Data – Historical and Prediction
Control system behavior and logic (HOOTL)
RCS Propellant Mass
Launch Site
6DoF Model of Balloon and Launch Structure (approx. as rigid bodies)
Farley Aero LLC balloon drift model
Software Toolsets
Data Inputs
ASTOS
STK launch ascent modeling possibly
Software Toolsets
Drift Ephemeris of Balloon
  Dispersion Analysis for worst-case cone
  Incorporate zero-pressure
Attitude Dynamics of Balloon/Launch Structure system
  Dispersion Analysis of rocket pointing
Launch Structure/Balloon descent ephemeris
Data Outputs
Using launch structure/balloon metrics, input to Farley’s balloon drift model or possibly an internal model to generate ephemeris
  Run model >50 times for dispersion analysis and generate a range of “end points”
  Use range of end points to generate a cone of likely/possible trajectories
In final ascent portion, implement control logic into 6DoF behavior of launch structure and balloon
  Run model >50 times for dispersion analysis generate a pointing cone of possibility
Mod-Sim Logic
Balloon Trajectory Cone
Rocket Pointing Cone
3D Model of Rocket
Engine parameters
Staging splits
Control system behavior and logic (HOOTL)
RCS Propellant Mass
Data Inputs
Sample ~10 points (maybe less?) from within balloon trajectory cone to represent dispersion possibilities
From each point, sample 5 points from rocket pointing cone
From each individual balloon/rocket pointing instance, model and optimize an ascent trajectory to orbit using rocket design parameters
  Utilize theoretical rocket control algorithm
From these two levels of dispersion, generate a range of ~50 orbit insertion points and corresponding final orbit
Mod-Sim Logic
Range of possible orbit injection locations and final orbital parameters
Optimized ascent trajectory ephemeris
6DoF Dynamics of Rocket
  Dispersion Analysis of rocket pointing and control
Pressure and Thermal effects on rocket during ascent
Data Outputs
ASTOS orbit modeling
STK orbit modeling
DAS or FreeFlyer?
Software Toolsets
Range of orbital insertion parameters
CubeSat design
Atmospheric data – historical and prediction
Data Inputs
Sample ~10 points (maybe less?) from within orbital insertion parameter set to represent dispersion possibilities
From each initial orbit, model the orbit evolution and decay time along with comms interactions
  Attempt to model CubeSat spin (If we have a control algorithm to control attitude? May be necessary for comms link with constellation.)
Model rocket 1st stage deorbit trajectory (not sure how yet)
Model rocket 2nd stage deorbit trajectory (not sure how yet)
Mod-Sim Logic
Range of possible orbit injection locations and final orbital parameters
Duration of CubeSat final orbit
6DoF Dynamics of CubeSat
  Spin rate most important parameter
Effects on thermal and power
Data Outputs

## Slide 2
MASTRAB – Modeling and Simulating Trajectories of Rocket and Balloon
Run Mode Options:
Independent Model Options:
  Single Run Options:
    Ground to Rocket Launch
    Rocket Launch to Orbit Injection
    Orbit Injection to Deorbit
  N-Variable Linear Trade Study Option
  Random Dispersion Study Option
Integrated Multi-Model Options:
  Single Run Options:
    Ground to Orbit Injection
    Rocket Launch to Deorbit
    Ground to Deorbit
  N-Variable Linear Trade Study Option
  Random Dispersion Study Option
Available Models:
Balloon/LS 6DOF
  Balloon Drift Model
  Balloon/LS Attitude Model
Rocket Sizing Model
Rocket Ascent Model
Orbital 6DOF Model
  Orbit Propagation Model
  Satellite Attitude Model

## Slide 3
MASTRAB Framework Wants vs. Needs
Needs for Fall 2021
Run Mode Options:
Independent Model Options:
  Single Run Options:
    Ground to Rocket Launch
  N-Variable Linear Trade Study Option
Wants for the Future
Run Mode Options:
Independent Model Options:
  Single Run Options:
    Ground to Rocket Launch
  Random Dispersion Study Option
Integrated Multi-Model Options:
  Single Run Options:
    Ground to Orbit Injection
    Rocket Launch to Deorbit
    Ground to Deorbit
  N-Variable Linear Trade Study Option
  Random Dispersion Study Option

## Slide 4: Breakdown of Balloon Modeling Push
High level code framework in Git/Python
Historical wind data (can be localized in space/time for initial work)
  Build robust interface scripts to query later
Basic "balloon always follows wind perfectly" to start
Propagator to write ephemeris files (*.e) for STK analysis
Balloon 6DOF model
Balloon fluids model
  Is it needed?
  Compare with basic drift model
Balloon expansion model
  Morph models from sea level balloon -> equilibrium balloon
  Note impact on fluids model drift predictions

## Slide 5: Tasks to complete pre-onboarding
High-level picture of framework (cheesy acronym needed) documented on repository readme
  How will different mission phases interact?
  How will models/scripts plug into the framework?
  What dependencies do we expect to need external to the repository (STK, ASTOS, weather data, etc)?
Discuss how we'll balance onboarding with beginning real development work as a team